## Slide 1
Faculty of Engineering & Information Technology Al-AZHAR UNIVERSITY-GAZA Digital Signal Processing (DSP) (ITCC 4325)
Teacher Assistant: Eng. Dalia Tariq Alhindi Supervised by: Dr. Ali Awad

## Slide 2
Objectives:
What is MATLAB ?
How to install MATLAB?
Basic Instructions in Mat lab.
Generation of basic signals.
Samples.
Basic operations on discreet signals.

## Slide 3
What is MATLAB ?
Is a programming platform designed specifically for engineers and scientists.
The heart of MATLAB is the MATLAB language.
a matrix-based language allowing the most natural expression of computational mathematics.
What can you do with MATLAB?
Using MATLAB, you can:
Analyze data.
Develop algorithms.
Create models and applications.

## Slide 4
Who uses MATLAB?
Millions of engineers and scientists in industry and academia use MATLAB.
MATLAB applications:
Deep learning ,
machine learning ,
signal processing and communications,
image and video processing,
control systems,
test and measurement,
computational finance,
and computational biology.

## Slide 5
Basic Instructions in Matlab :
T = 0: 1:10
Explanation :This instruction indicates a vector T which as initial value 0 and final value 10 with an increment of 1
Output: T = [0 1 2 3 4 5 6 7 8 9 10]
2. zeros (1, 3)
Explanation : The above instruction creates a vector of one row and three columns whose values are zero .
Output: [0 0 0]

## Slide 6
3. ones (5,2)
Explanation : The above instruction creates a vector of five rows and two columns .
Output: 1 1
1 1
1 1
1 1
1 1
a = [ 1 2 3] b = [4 5 6] c= a.*b
Explanation : array product element by element.
Output: c= [4 10 18]
Notes: Discussion : What is the different between a*b and a.*b?

## Slide 7
5.plot (t, x)
Explanation : Ifx = [6 7 8 9] t = [1 2 3 4] This instruction will display a figure window which indicates the plot of x versus t.
Output:
6.stem (t,x)
Output:

## Slide 8
7.Subplot
Explanation : This function divides the figure window into rows and columns. Subplot (2 2 1) divides the figure window into 2 rows and 2 columns 1 represent number of the figure
Subplot (3 1 2) divides the figure window into 3 rows and 1 column 2 represent number of the figure .

## Slide 9
8.xlabel Syntax: xlabel('string') Description: xlabel('string') labels the x-axis of the current axes.
9. ylabel Syntax : ylabel('string') Description: ylabel('string') labels the y-axis of the current axes
10.Title Syntax : title('string') Description: title('string') outputs the string at the top and in the center of the current axes.
11.grid on Syntax : grid on Description: grid on adds major grid lines to the current axes.
Notes: سؤال :
C = A.*B multiplies arrays A and B element by element and returns the result in C.
A = [1 0 3]; B = [2 3 7]; C = A.*B
C=2 0 21
C=A*B >>> errore why?

## Slide 10
Generation of basic signals:
1. Unit impulse signal. 2. Unit step signal. 3. Unit ramp signal. 4. Exponential growing signal. 5. Exponential decaying signal. 6. Sine signal. 7. Cosine signal.
8. Random Signals.

## Slide 11
1. Unit impulse signal.
clc; clear all; close all; dis p('UNIT I MPUL SE SIGNAL '); N=input(' E nter Number of Samples: '); n=-N:1:N x=[zeros(1,N) 1 ze ros(1,N)] stem(n,x); xlabel('Time'); ylabel('Amplitude'); title('Impulse Response');

## Slide 12
2. Unit step signal.
clc; clear all; close all; dis p('UNIT STE P SIGN AL'); N=input(' Enter Number of Samples : '); n=-N:1:N x=[zeros(1,N) 1 ones (1,N)] stem(n,x); xlabel('Time'); ylabel('Amplitude'); title('Unit Ste p Response');

## Slide 13
3. Unit ramp signal.
clc; clear all; close all; dis p('UNIT RA MP SIGN AL'); N=input(' Enter Number of Samples : '); a=input('Enter Amplitude : ') n=0:1:N x=a *n stem(n,x); xlabel('Time'); ylabel('Amplitude'); title('Unit Ramp Response');

## Slide 14
4. Exponential decaying signal.
clc; clear all; close all; dis p('E XPONE NT IAL DE C AYING SIGNAL '); N=input(' Enter Number of Samples : '); a=0.5 n=0:.1:N x=a.^ n stem(n,x); xlabel('Time'); ylabel('Amplitude'); title('Exponential Decaying Signal Response');

## Slide 15
5. Exponential growing signal.
clc; clear all; close all; dis p('E XPONE NT IAL GR O WING SIGNAL '); N=input(' Enter Number of Samples : '); a=0.5 n=0:.1:N x=a.^ -n stem(n,x); xlabel('Time'); ylabel('Amplitude'); title('Exponential Growing Signal Response');

## Slide 16
6. Cosine signal.
clc; clear all; close all; dis p('COSINE SIGNAL '); N=input(' Enter Number of Samples : '); n=0:.1:N x=cos(n) stem(n,x); xlabel('Time'); ylabel('Amplitude'); title('Cosine Signal');

## Slide 17
7. Sine signal. clc; clear all; close all; dis p('SINE SIGNAL '); N=input(' Enter Number of Samples : '); n=0:.1:N x=sin(n) stem(n,x); xlabel('Time'); ylabel('Amplitude'); title('sine Signa l');

## Slide 18
8.Random Signals:
A random signal of length N with samples uniformly distributed in the interval (0,1) can be generated by using the MATLAB command
            x = rand(1,N);
a random signal x[n] of length N with samples normally distributed with zero mean and unity variance can be generated by using the following MATLAB command
            x = randn(1,N);

## Slide 19
Write a MATLAB program to generate and display a random signal of length 100 whose elements are uniformly distributed in the interval [−2, 2].
Write a MATLAB program to generate and display a Gaussian random signal of length 75 whose elements are normally distributed with zero mean and a variance of 3.
Home WORK:
HINT:
standard deviation = sqrt(variance); x = standard deviation *randn(1,N)+ mean;

## Slide 20
Implementation :
generate the following sine sígnalas then find the sumation of signals.
  y1=sin(t); y2=sin(3*t)/3; y3=sin(5*t)/5; y4=sin(7*t)/7; y5=sin(9*t)/9;

## Slide 21
Solution :
clc; clear all; close all; tic; t=0:.01:pi; %generation of sine signals y1=sin(t); y2=sin(3*t)/3; y3=sin(5*t)/5; y4=sin(7*t)/7; y5=sin(9*t)/9; y = sin(t) + sin(3*t)/3 + sin(5*t)/5 + sin(7*t)/7 + sin(9*t)/9; plot(t,y,t,y1,t,y2,t,y3,t,y4,t,y5); legend('y','y1','y2','y3','y4','y5'); title('generation of sum of sinusoidal signals');grid; ylabel('---> Amplitude'); xlabel('---> t'); toc;
NOTE: tic & toc Start a stopwatch timer. The sequence of commands
Notes: صوت الانسان عبارة عن مجموعة من التون بالتالي صوت الانسان عبارة عن عدد لانهائي من ال sine signals

## Slide 22
daliaaug2019@gmail.com